## Slide 1
NHAI · INDIAN FACE DATASET
Offline Face Auth
Post-Demo Review
End-to-end architecture · Security framework · Datalake integration
July 2026 · Live demo at NHAI

## Slide 2
ARCHITECTURE
Offline-first, sync-when-connected
The device runs fully offline. Attendance records sync to the cloud when connectivity is available.
Mobile App
RN 0.74 · TFLite EdgeFace-S
Face detect + recognition
Active + passive liveness
Offline queue, encrypted
Sync Service
Batch POST via NetInfo
X-API-Key guarded
Retries with backoff
Purges on server ack
Backend API
Express + TypeScript
store.ts integrity guard
Rate-limit 30/min/device
Cross-device collision detect
Datalake & Admin
PostgreSQL sharded
Admin web dashboard
KPI tracking
Alerting & reporting
→
→
→
KEY FLOW
1. Face detected → TFLite recognition + liveness → attendance record queued locally
2. NetInfo triggers sync → pending records POSTed to backend
3. Backend validates (guard), stores to PostgreSQL, returns ack
4. Device purges only acknowledged records — no data loss
OFFLINE RESILIENCE
MMKV-encrypted on-device queue
No data left behind on network loss
Batch size capped (SYNC.batchSize)
Auto-retry on next app launch
All processing is on-device. The backend never sees raw video or embeddings — only verified attendance records.

## Slide 3
SECURITY
Defence-in-depth across device & cloud
Active Liveness
Randomised blink/smile/turn
challenge, 2-of-4 per attempt.
Motion-range defeat for
static photos.
Passive Anti-Spoof
MiniFASNet on-device TFLite
model. Screen/print replay
detection via texture analysis.
Configurable thresholds.
Escalation Lockout
On-device: 5 consecutive
failures → lockout 1m, 2m, 4m
(exponential). Prevents
brute-force presentation.
Backend Guard
store.ts guard(): score sanity,
monotonic timestamps, rate
limit 30/min/deviceId, cross-
device collision detection.
ATTACK SURFACE COVERAGE
3
Anti-spoof layers
30/min
Rate limit / device
Exponential
Lockout escalation
Guard()
All write paths
All blocking events are persisted to the attendance queue and synced — zero blind spots.

## Slide 4
DATALAKE
Central nervous system for site-level & cross-site analytics
DATA FLOW
Attendance records flow: Each verified (or blocked) attend is queued on-device, synced to the backend on connectivity, and written to the sharded PostgreSQL database. The admin web dashboard exposes real-time KPIs — liveness pass rate, attack count, site-level attendance, and per-device guard violations.
WHAT IT ENABLES
Cross-site attendance aggregation
Real-time liveness pass-rate monitoring
Attack-pattern detection per device / site
Geofence compliance dashboards
Alerting: guard violations, low pass rates
SAMPLE DASHBOARD KPIs
9,708
Enrolled identities
27k+
Daily attend records
≥99%
Liveness pass rate
Blocked
Per-attack reporting
DATALAKE PIPELINE
Device (offline queue) → Sync POST → Backend guard() / validate → PostgreSQL (sharded by month) → Admin dashboard → Export / reporting pipeline
All data carries deviceId, userId, livenessPassed, geofence info — every record is actionable.

## Slide 5
NEXT STEPS
Hardening & scale
Passive liveness calibration
Field-collect MiniFASNet score distributions to set thresholds that block attacks without false-rejecting real users. Then enable REQUIRE_PASSIVE_LIVENESS and PASSIVE_SCREEN_BLOCK.
Datalake expansion
Add analytics pipeline for trend analysis, anomaly detection, and automated alerting rules per site / device.
Admin dashboard enhancements
Role-based access, drill-down to individual attendance records, geofence zone management via the web UI.
Scale testing
Benchmark under load: 100+ concurrent devices, partitioned PostgreSQL, proxy-worker sharding for horizontal scale.
Penetration testing
Third-party security audit targeting on-device liveness bypass, sync-channel tampering, and backend API abuse.
NHAI · Offline Face Auth · July 2026